## Slide 1: A Measurement Study of RDMA Performance In Multi-Tenant Environment - VMs and Containers
Student: Zhuangdi Zhu Supervisor: Alex Liu
Mentors: Salman A Baset Michael R Hines
Dec 9th, 2014

## Slide 2: RDMA
RDMA provides high-throughput, low-latency networking:
  Reduce consumption of CPU cycles
  Reduce communication latency
Notes: RDMA is the ability of accessing( i.e. reading from or writing to) on a remote machine without interrupting the processing of CPU(s) on that system.

## Slide 3: RDMA
Three protocols support RDMA:
InfiniBand (IB)
RDMA Over Converged Ethernet (RoCE)
Internet Wide Area RDMA Protocol (iWARP)
Application
TCP
IP
Ethernet Link
Application
OFA software
IB transport
Ethernet Link
Application
OFA software
IB transport
IB link
TCP
RoCE
InfiniBand

## Slide 4: InfiniBand (IB)
a new generation network protocol which supports RDMA natively from the beginning. it requires NICs and switches which supports this technology.
 High throughput
 Low latency
 Quality of service
 Fail over
 Scalability
 Reliable transport

## Slide 5: RDMA over Converged Ethernet (RoCE)
a network protocol which allows performing RDMA over Ethernet network.
Its lower network headers are Ethernet headers and its upper network headers (including the data) are InfiniBand headers. This allows using RDMA over standard Ethernet infrastructure (switches). Only the NICs should be special and support RoCE.

## Slide 6: Internet Wide Area RDMA Protocol (iWARP)
a network protocol which allows performing RDMA over TCP.
There are features that exist in IB and RoCE and aren't supported in iWARP. This allows using RDMA over standard Ethernet infrastructure (switches).
Only the NICs should be special and support iWARP (if CPU offloads are used) otherwise, all iWARP stacks can be implemented in SW and loosing most of the RDMA performance advantages

## Slide 7: Proposed Experiment Paths
scenario | sender | receiver | protocol | test
1 | host | host | TCP | 1 and 4 transfers
2 | host | host | RDMA | 1 and 4 transfers
3 | VM | VM | TCP | 1 and 4 transfers
4 | VM | VM | RDMA | 1 and 4 transfers
5 | LXC | LXC | TCP | 1 and 4 transfers
6 | LXC | LXC | RDMA | 1 and 4 transfers
7 | 4 VMs | 4 VMs | TCP | 1 transfer
8 | 4 VMs | 4 VMs | RDMA | 1 transfer
9 | 4 LXCs | 4 LXCs | TCP | 1 transfer
10 | 4 LXCs | 4 LXCs | RDMA | 1 transfer

## Slide 8: Reading List
List No. | Title | Status
1 | Accelerating Spark with RDMA for Big Data Processing: Early Experiences | read
2 | IBM Zurich – RDMA | 
3 | Hadoop RDMA | 
4 | Accelerating Big Data with RDMA solutions | read
5 | Features/RDMALiveMigration - QEMU | 
6 | RDMA Consortium | 
Papers/Slides/Websites

## Slide 9: Reading List
List No. | Title | Status
7 | RFC5532 - Network File System (NFS) Remote Direct Memory Access (RDMA) Problem Statement | 
8 | RFC5041 - Direct Data Placement over Reliable Transports | 
9 | RFC5042 - Direct Data Placement Protocol (DDP) / Remote Direct Memory Access Protocol (RDMAP) Security | read 2 pages
10 | RFC5040 - A Remote Direct Memory Access Protocol Specification | 
11 | RFC7146 - Securing Block Storage Protocols over IP: RFC 3723 Requirements Update for IPsec v3 | 
RFC Documents

## Slide 10: Reading List
List No. | Title | Status
12 | Z-Copy Education and Sample Code for RDMA Programminghttp://zcopy.wordpress.com/2010/10/08/quick-concepts-part-1-%E2%80%93-introduction-to-rdma/ | read
13 | Introduction to Remote Direct Memory Access (RDMA)http://www.rdmamojo.com/2014/03/31/remote-direct-memory-access-rdma | read
14 | Working with RDMA in RedHat/CentOS 6.* http://www.rdmamojo.com/2014/09/20/working-rdma-redhatcentos-6/ | read
15 | RDMA Performance in Virtual Machines using QDR InfiniBand on Vmware http://www.mellanox.com/related-docs/whitepapers/RDMA_Performance_in_Virtual_Machines_using_QDR_InfiniBand_on_VMware_vSphere5.pdf | read
16 | Access to InfiniBand* from Linux* https://software.intel.com/en-us/articles/access-to-infiniband-from-linux/ | read
Resources from Google Search

## Slide 11: Test Environment
Host Hardware | MacBook Air
Host OS | OS X 10.9.5 (13F34)
Processor | 1.4 GHz Intel Core i5 Dual Core
Memory | 4 GB 1600 MHz DDR3
VM Software | VirtualBox 4.3.20
Guest OS | Linux CentOS 6.5
Linux Kernel Version | 2.6.32-431.el6.x86_64
OFA OFED | Open Fabrics Alliance OFED(3.12/3.5) (failed)
Guest Memory | 1 GB

## Slide 12: Proposed Methodology
Set up a pair of nodes for each protocol: RDMA(RoCE or iWARP) and TCP.
Install, configure & run minimal services on test nodes to maximize machine performance.
Directly connect nodes to maximize network performance.
Write program / use existing benchmark to test data transfer using TCP and RDMA.
Install single guest VM on each node, repeat the above steps.
Install four guest VMs on each node, repeat the above steps.

## Slide 13: Work I have done
Read Documents/Web resources about RDMA
Installed VirtualBox on Macbook
Installed CentOS 6.5 as Guest OS and basic utilities
Read materials about RoCE
Experiments:
tried to install Open Fabrics Alliance OFED(3.12 and 3.5) but it seems in-compatible with Linux version(CentOS 6.6 and 6.5).

## Slide 14: Difficulties
I Don’t Have Hardware Resource for Experiments
  Only one MacBook without Ethernet Card
  RDMA required RDMA-enabled Network Adapter
  Seems only SoftRoCE or SoftiWARP can be used at this moment
Finding the right versions of OS, OFED, drivers that work together
  E.g., OFA OFED doesn’t support CentOS 6.6
How to fix the errors or problems during installation and compilation (OFED, RoCE ..)
Work with Linux kernel, modules and drivers

## Slide 15: TODO
Install SoftRoCE in Virtualbox

## Slide 16: Backup slides

## Slide 17
Your Application
Socket Layer
TCP
UDP
IP
Ethernet Driver
Adapter Driver
RDMA Enabled Channel Adapter Card
uverbs
Kernel mod
Verbs API
Traditional Network Interface
Command Channel
Data Channel
User Space
Kernel

## Slide 18: A Measurement Study of RDMA Performance In Multi-Tenant Environment - VMs and Containers
Student: Zhuangdi Zhu Supervisor: Alex Liu
Mentors: Salman A Baset Michael R Hines
Dec 15th, 2014

## Slide 19: Work I have done
Installed CentOS-6.5-x86_64 as Operating System on two real hosts.
Installed the right kernel-devel (2.6.32-431.el6.x86_64).
Installed openmpi and finished the first experiment (host to host , 1 transfer, using tcp).
Equipped the two hosts with InfiniBand Adapter cards(CX353A).
Installed OFED-3.12 successfully.
Tried to connect the two hosts directly using one InfiniBand cable but failed.

## Slide 20: Steps
#ssh 192.168.1.104 (ssh 192.168.1.103)
# yum install rpm-build libtool zlib-devel libstdc++-devel gcc-c++ bison flex tcl tk glib2-devel tcl-devel git
#uname –r
2.6.32-431.el6.x86_64
#wgethttp://vault.centos.org/6.5/os/x86_64/Packages/kernel-devel-2.6.32-431.el6.x86_64.rpm
#useradd test
#passwd test
#su test
#cd
#yum –y install openmpi-devel
#cd openmpi-1.8.3
#./configure --prefix=/home/test/openmpi
#make
#make install

## Slide 21
# wget http://downloads.openfabrics.org/downloads/OFED/ofed-3.12/OFED-3.12.tgz
#cd OFED-3.12
#./install.pl
#vim transfer1.c
#mpicc transfer1.c –o transfer1
#mpirun -np 2 hostname
#mpirun -np 2 -host zhuangdizhu1,zhuangdizhu2 hostname
#mpirun -np 2 -host zhuangdizhu1 ./transfer1
Steps

## Slide 22
#mpirun -np 2 -host zhuangdizhu1,zhuangdizhu2 ./transfer1
#ifconfig ib0
ib0 Link encap:InfiniBand HWaddr 80:00:00:48:FE:80:00:00:00:00:00:00:00:00:00:00:00:00:00:00
BROADCAST MULTICAST MTU:4092 Metric:1
RX packets:0 errors:0 dropped:0 overruns:0 frame:0
TX packets:0 errors:0 dropped:0 overruns:0 carrier:0
collisions:0 txqueuelen:256
RX bytes:0 (0.0 b) TX bytes:0 (0.0 b)
Steps

## Slide 23
#vim /etc/sysconfig/network-scripts/ifcfg-ib0
Add the following:
#ONBOOT=yes
BOOTPROTO=static
IPADDR=192.168.1.2(192.168.1.3 for the other host)
NETMASK=255.255.255.255
GATEWAY=192.168.1.1
Steps

## Slide 24
#vim /etc/sysconfig/network-scripts/ifcfg-eth0
#service network restart
#route
#route add 192.168.1.1 dev ib0
#route add default gw 192.168.1.1
#route
#ping 192.168.1.2
Steps

## Slide 25: Backup slides

## Slide 26: A Measurement Study of RDMA Performance In Multi-Tenant Environment - VMs and Containers
Student: Zhuangdi Zhu Supervisor: Alex Liu
Mentors: Salman A Baset Michael R Hines
Dec 20th, 2014

## Slide 27: Sequence diagram for RDMA client-server file transfer:
  Post receive Start listening
  Initiate connection
Accept connection Post receive
Send memory region details
Re-post receive
RDMA-write file name
Open file descriptor
Re-post receive
Send ready-to-receive
Re-post-receive
Read chunk from file RDMA-write chunk
Write chunk to file
Re-post receive
Send ready-to-receive
Re-post-receive
RDMA-write zero bytes
Send done
Close connection
Chose file secriptor
Client
Server

## Slide 28: Reading List
List No. | Title | Status
1 | Intro_to_IB_for_End_Users | Read chapter 1, 4 and most part of chapter 5
2 | building-an-rdma-capable-application-with-ib-verbs | Read part 1( Basics), and roughly read part 2(source code for server side) and 3(source code for client side)
3 | rdma-read-and-write-with-ib-verbs | Same as above
4 | basic-flow-control-for-rdma-transfers | Adjusted the sample code it provided and used it to finish a single rdma transfer
5 | Introduction to Sockets Programming in C using TCP/IP | Read the first 30 pages

## Slide 29: Work I Have Done
Test rdma/tcp bandwidth and latency using qperf to obtain a basic understanding of the performance difference between TCP and RDMA
Qperf：
qperf measures bandwidth and latency between two nodes. It can work over TCP/IP as well as the RDMA transports. On one of the nodes, qperf is typically run with no arguments designating it the server node. One may then run qperf on a client node to obtain measurements such as bandwidth, latency and cpu utilization.

## Slide 30: Work I Have Done
Test rdma/tcp bandwidth and latency using qperf
[root@zhuangdizhu1 ~]# qperf
[root@zhuangdizhu2 ~]# for i in {1..10}; do qperf zhuangdizhu1 rc_rdma_read_lat; done
[root@zhuangdizhu2 ~]# for i in {1..10}; do qperf zhuangdizhu1 rc_rdma_read_bw; done
[root@zhuangdizhu2 ~]# for i in {1..10}; do qperf zhuangdizhu1 rc_rdma_write_bw; done
[root@zhuangdizhu2 ~]# for i in {1..10}; do qperf zhuangdizhu1 rc_rdma_write_lat; done
[root@zhuangdizhu2 ~]# for i in {1..10}; do qperf zhuangdizhu1 tcp_bw; done
[root@zhuangdizhu2 ~]# for i in {1..10}; do qperf zhuangdizhu1 tcp_lat; done

## Slide 31: Work I Have Done
Results | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | Avg
Rdma_read-lantency(us) | 3.98 | 4.08 | 4.03 | 4.04 | 4.05 | 4.06 | 3.91 | 4.07 | 4.04 | 4.04 | 4.03
Rdma_read-bandwidth (GB/sec) | 3.82 | 3.81 | 3.82 | 3.82 | 3.82 | 3.82 | 3.82 | 3.82 | 3.82 | 3.82 | 3.819
Rdma_write-lantency(us) | 10.7 | 10.8 | 10.8 | 10.8 | 10.7 | 10.6 | 10.8 | 10.8 | 10.8 | 10.8 | 10.76
Rdma_write-bandwidth (GB/sec) | 3.74 | 3.75 | 3.74 | 3.75 | 3.75 | 3.76 | 3.75 | 3.75 | 3.75 | 3.75 | 3.749
Tcp_bandwidth(MB/sec) | 11.9 | 11.9 | 11.9 | 11.9 | 11.9 | 11.9 | 11.9 | 11.9 | 11.9 | 11.9 | 11.90
Tcp_latency (us) | 36.8 | 36.8 | 36.8 | 36.8 | 36.9 | 36.8 | 36.8 | 36.8 | 36.8 | 36.8 | 36.81
Table 1. Comparison of RDMA and TCP using qperf

## Slide 32: Comparisons
Chart: Comparison of latency
| tcp | rc_rdma_read | rc_rdma_write
 | 36.81 | 4.03 | 10.76
Chart: Comparison of bandwidth
| tcp | rc_rdma_read | rc_rdma_write
 | 0.011 | 3.819 | 3.746

## Slide 33: Work I Have Done
Finished the experiment of RDMA single transfer using lower-level-programming rather than MPI.
results | No.1 | No.2 | No.3 | No.4 | No.5 | No.6 | No.7 | No.8 | No.9 | N.10 | Avg
Rdma single transfer (sec) | 1.154 | 1.157 | 1.155 | 1.142 | 1.151 | 1.154 | 1.157 | 1.155 | 1.159 | 1.216 | 1.160
Table 2. Time for client transferring 1GB file to server

## Slide 34: Work I Have Done
#vim Makefile
LDFLAGS := ${LDFLAGS} -lrdmacm -libverbs –lrt
#vim client.c
#include <time.h>
…………
…………
int main(int argc, char **argv)
{
…………
…………
clock_gettime(CLOCK_REALTIME,&t1);
rc_client_loop(argv[1], DEFAULT_PORT, &ctx);
clock_gettime(CLOCK_REALTIME, &t2);
diff = (double) (t2.tv_sec-t1.tv_sec) + (double) (t2.tv_nsec-t1.tv_nsec) / 1e9;
printf("%lf\n", diff);
close(ctx.fd);
return 0;
}
Precise Timing (nano secs)

## Slide 35: Work I Have Done
[test@zhuangdizhu1 rdma-file-transfer]$ ./server
waiting for connections. interrupt (^C) to exit.
opening file test-file
received 10485760 bytes.
received 10485760 bytes.
……
received 10485760 bytes.
received 10485760 bytes.
received 4194304 bytes.
finished transferring test-file
[root@zhuangdizhu2 rdma-file-transfer]# dd if=/dev/zero of=test-file bs=1M count=1024
[root@zhuangdizhu2 rdma-file-transfer]# ./client 172.16.1.2 test-file
received MR, sending file name
received READY, sending chunk
received READY, sending chunk
……
received READY, sending chunk
received READY, sending chunk
received DONE, disconnecting
1.155221

## Slide 36: Work I Have Done
Read documents, try to understand and tune the /proc/sys/net/ipv4/tcp_** parameters (rmem, wmem, etc)
Try to find a sample code for tcp socket programming but have not found one yet

## Slide 37: Difficulties
I want to use a higher-level program to make it easier to code, e.g. MPI, but there is something wrong with my openmpi version .
It works when the program runs on one host , and works as well on two hosts when it runs hostname
[test@zhuangdizhu2 ~]$ mpirun -np 2 -host zhuangdizhu2 --report-bindings --mca btl self,sm,openib ./transfer1
[zhuangdizhu2:13201] MCW rank 1 bound to socket 0[core 1[hwt 0-1]]: [../BB/../..]
[zhuangdizhu2:13201] MCW rank 0 bound to socket 0[core 0[hwt 0-1]]: [BB/../../..]
time per 1GB: 0.614994 secs
[test@zhuangdizhu2 ~]$
[test@zhuangdizhu2 ~]$ mpirun -np 2 -host zhuangdizhu2,zhuangdizhu1 --report-bindings --mca btl self,sm,openib hostname
[zhuangdizhu2:13186] MCW rank 0 bound to socket 0[core 0[hwt 0-1]]: [BB/../../..]
zhuangdizhu2
[zhuangdizhu1:04666] MCW rank 1 bound to socket 0[core 0[hwt 0-1]]: [BB/../../..]
zhuangdizhu1
However, openmpi cannot identify openib as a component:

## Slide 38: Difficulties
And It will not show any results when using tcp network:
[test@zhuangdizhu2 ~]$ mpirun -np 2 -host zhuangdizhu2,zhuangdizhu1 --report-bindings --mca btl self,sm,tcp ./transfer1
[zhuangdizhu2:13218] MCW rank 0 bound to socket 0[core 0[hwt 0-1]]: [BB/../../..]
[zhuangdizhu1:04699] MCW rank 1 bound to socket 0[core 0[hwt 0-1]]: [BB/../../..]
^CKilled by signal 2.
[zhuangdizhu1][[29789,1],1][btl_tcp_frag.c:215:mca_btl_tcp_frag_recv] mca_btl_tcp_frag_recv: readv failed: Connection reset by peer (104)

## Slide 39: A Measurement Study of RDMA Performance In Multi-Tenant Environment - VMs and Containers
Student: Zhuangdi Zhu Supervisor: Alex Liu
Mentors: Salman A Baset Michael R Hines
Dec 22th, 2014

## Slide 40: Virtio
An abstraction layer over devices in a paravirtualized hypervisor

## Slide 41: Virtio
virtio is an abstraction for a set of common emulated devices in a paravirtualized hypervisor.
export a common set of emulated devices and make them available through a common application programming interface (API).

## Slide 42: Device emulation
(full virtualization) (paravirtualization)
Guest Operating System
Hypervisor
(Full virtualization)
Traps
Device
Emulation
Hardware
Hypervisor
(Full virtualization)
Traps
Device
Emulation
Hardware
Guest Operating System
Para-drivers

## Slide 43: Driver abstractions with virtio
virtio
Linux guest
Front-end drivers
KVM
(Linux ypervisor)
Lguest
(Linux ypervisor)
Back-end drivers
Device emulation
Back-end drivers
Device emulation
Hardware

## Slide 44: Virtio architecture
(High-level architecture of the virtio framework)
virtio-blk
virtio-net
virtio-balloom
virtio-console
virtio
Transport
Virtio back-end
drivers
virtio-pcl

## Slide 45: Cgroups
Rule 1
A single hierarchy can have one or more subsystems attached to it
Rule 2
Any single subsystem (such as cpu) cannot be attached to more than one hierarchy if one of those hierarchies has a different subsystem attached to it already.